Game Boy Camera Technical Information v1.0

by Antonio Niño Díaz (AntonioND)
03/2015

Antonio Niño Díaz (AntonioND), 2014, 2015

This work is licensed under the Creative Commons Attribution 4.0 International License. To view a copy of this license, visit http://creativecommons.org/licenses/by/4.0/.
# Introduction
Since there is no documentation about the Game Boy Camera I decided it was time to document it. Some years ago, about
# The Game Boy Camera Cartridge
The Game Boy Camera cartridge contains 4 ICs: the usual ROM and RAM ICs, a big controller IC (like a MBC) and a sensor (M64282FP "retina" chip).
The main board contains all ICs except from the sensor. From gbdev wiki:
Component#	Part#/inscription	Description
U1	MAC-GBD / Nintendo / 9807 SA	I/O, memory control.
U2	GBD-PCAX-0 F / M538011-E - 08 / 8145507	1MB ROM
U3	52CV1000SF85LL / SHARP JAPAN / 9805 5 0A	128KB RAM

The U1 is the only one connected to the GB cartridge pins (besides some of the address pins of the ROM IC). The U2 and U3 (ROM and RAM) are connected to U1. The M64282FP "retina" chip is in a separate PCB, and is connected to the U1.
The M64282FP handles most of the configuration of the capturing process. The U1 transforms the commands from the Game Boy CPU into the correct signals needed for the M64282FP. The detailed timings are described below.
It is a good idea to have the datasheet of the M64282FP, but it is very poorly explained, so this document will try to explain everything about it (except from limits like voltage or signal timings). There are datasheets of similar sensors (M64283FP and M64285FP) that can be very useful to understand some things about the sensor of the GB Camera.
## Game Boy Camera MBC
The Game Boy Camera controller works pretty much the same as a MBC3.
0000-3FFF - ROM Bank 00 (Read Only)
First 16 KB of the ROM.
4000-7FFF - ROM Bank 01-3F (Read Only)
This area may contain any ROM bank (0 included). The initial mapped bank is 01.
A000-BFFF - RAM Bank 00-0F (Read/Write)
A000-BFFF - CAM Registers (Read/Write)
Depending on the current RAM Bank Number, this memory space is used to access the cartridge RAM or the CAM registers.
0000-1FFF - RAM Enable (Write Only)
A value of 0Ah will enable writing to RAM, 00h will disable it. Reading from RAM or registers is always enabled. Writing to registers is always enabled. Disabled on reset.
2000-3FFF - ROM Bank Number (Write Only)
Writing a value of 00-3Fh selects the corresponding ROM Bank for area 4000-7FFF.
4000-5FFF - RAM Bank Number/CAM Registers Select (Write Only)
Writing a value in range for 00h-0Fh maps the corresponding external RAM Bank to memory at A000-BFFF. Writing any value with bit 5 set to '1' will select CAM registers. Usually bank 10h is used to select the registers. All registers are mirrored every 80h bytes. RAM bank 0 selected on reset.
IMPORTANT NOTE: Unlike most games, the GB Camera RAM can only be written when PHI pin = '1'. It's an enable signal for the RAM chip. Most cartridge readers and writers can't handle PHI pin so they can't restore a saved backup. It isn't needed to change ROM banks.
## Game Boy Camera I/O Registers
The Game Boy Camera I/O registers are mapped to all banks with bit 4 set to '1'. The GB Camera ROM usually changes to bank 16 to use the registers.
There are 3 groups of registers:
- The first group is composed by the trigger register A000. This register starts the capture process and returns the current status (working/capture finished).
- The second group is composed by registers A001-A005, used to configure most parameters of the M64282FP sensor.
- The third group is composed by 48 registers that form a 4×4 matrix. Each element of the matrix is formed by 3 bytes. This matrix is used for contrast and dithering.
All registers are write-only, except the register A000. The other ones return 00h when read. The initial values of all registers on reset is 00h.
### Register A000
The lower 3 bits of this register are read/writeable. The other ones return '0'. Writing any value with bit 0 set to '1' will start the capturing process. Any write with bit 0 set to '0' is ignored.
The value of bits 1 and 2 affect the value written to registers 4, 5 and 6 of the M64282FP:
[A000]	[4]	[5]	[6]	[4]=P [5]=M [6]=X
1(001)	00h	01h	01h	Negative
3(011)	01h	00h	01h	Positive. This is what the GB Camera ROM uses.
5(101)	01h	02h	01h	Used for edge detection
7(111)	01h	02h	01h	Used for edge detection

Bit 0 of this register is also used to verify if the capturing process is finished. It returns '1' when the hardware is working and '0' if the capturing process is over.
When the capture process is active all RAM banks will return 00h when read, but the register A000 can still be read to know when the transfer is finished.
The capturing process can be stopped by writing a '0' to bit 0. When a '1' is written again it will continue the previous capture process with the old capture parameters, even if the registers are changed.
### Register A001
This register is mapped to register 1 of M64282FP. It controls the output gain and the edge operation mode.
### Registers A002, A003
This registers are mapped to registers 2 and 3 of M64282FP. They control the exposure time. Register 2 is the MSB, register 3 is the LSB.
u16 exposure_steps = [A003] | ([A002]<<8);
### Register A004
This register is mapped to register 7 of M64282FP. It sets the output voltage reference, the edge enhancement ratio and can invert the image.
### Register A005
This register is mapped to register 0 of M64282FP. It sets the output reference voltage and enables the zero point calibration.
### Registers A006-A035
Those registers form a 4×4 matrix with 3 bytes per element. They handle dithering and contrast, and they are sorted by rows:
	X
Y	00	10	20	30
	01	11	21	31
	02	12	22	32
	03	13	23	33

A006	A007	A008	A009	A00A	A00B	A00C	A00D	A00E	A00F	A010	A011
D00L	D00M	D00H	D10L	D10M	D10H	D20L	D20M	D20H	D30L	D30M	D30H
A012	A013	A014	A015	A016	A017	A018	A019	A01A	A01B	A01C	A01D
D01L	D01M	D01H	D11L	D11M	D11H	D21L	D21M	D21H	D31L	D31M	D31H
A01E	A01F	A020	A021	A022	A023	A024	A025	A026	A027	A028	A029
D02L	D02M	D02H	D12L	D12M	D12H	D22L	D22M	D22H	D32L	D32M	D32H
A02A	A02B	A02C	A02D	A02E	A02F	A030	A031	A032	A033	A034	A035
D03L	D03M	D03H	D13L	D13M	D13H	D23L	D23M	D23H	D33L	D33M	D33H

This values are used for the contrast and dithering effects in the following way for each pixel at position (X,Y):
- The sensor outputs an analog value. This value is compared to the corresponding group of 3 values of the matrix probably using 3 DACs and 3 comparators (clock timings doesn't affect the result when converting from analog to digital, most ADCs would be affected).
- This value is compared to the corresponding group of 3 values of the matrix. To know what group of 3 values to use do (X mod 4) and (Y mod 4).
- The controller performs the following operations:
if ( sensor_value < DxyL ) gb_shade = black;
else if ( sensor_value < DxyM ) gb_shade = dark_gray;
else if ( sensor_value < DxyH ) gb_shade = light_gray;
else gb_shade = white;

This means that the minimum value to show a different color than white is 01h. A value of 00h in the 3 values will always show a white screen. A value of FFh in the 3 bytes will always allow some white pixels in a black background.
If two values are the same, the second comparison will be ignored. If the values are reversed (the higher bytes have lower values) that values are ignored. The previous comparisons explain that kind of behaviors.
To disable dithering all groups of 3 values must be the same. Dithering is obtained by doing small variations in the values of each one of the 4×4 groups.
The digital-to-analog conversion is not linear in the sense that a signal of 0V doesn't correspond to a digital value of 00h, it's affine: A value of 00h is around 0.8V and a value of FFh is around 4.1V. Note that the sensor has a 5.0V supply. That means that the value range is aproximately 3.3V, but it can't be reached by the sensor output. The sensor can only output from aproximately 0.9V to 4.0V (by modifying Vref and other configuration values). The previous limits have been determined by extrapolating, since the values are completely linear (if the offset at 00h is ignored).
According to the sensor datasheet the output voltage range is 2.0V peak to peak (102 in digital). The actual range seems to be up to 3.15V depending on the register configurations. That's the range of values that the controller has to convert into 4 Game Boy grey shades.
## Game Boy Camera timings
The capture process is started when the A000 register of the Game Boy Camera cartridge is written any value with bit 0 set to '1'.
The Game Boy Camera cartridge is one of the few cartridges that use the PHI signal (clock from the GB). That signal is a 1MHz clock (1048576 Hz). The M64282FP chip needs a clock input too, which is half the frequency of the PHI pin (0.5 MHz, 524288Hz). The reason for that is that the sensor chip sometimes handles the signals on the rising edge of the clock but other times on the falling edge. NOTE: This means that the GB Camera shouldn't be used in GBC double speed mode!
The time needed to capture and process an image depends on the exposure time and the value of the N bit of the register 1 of the M64282FP chip.
In GAME BOY CYCLES (1MHz):
N_bit = ([A001] & BIT(7)) ? 0 : 512
exposure = ([A002]<<8) | [A003]

CYCLES = 32446 + N_bit + 16 * exposure

Divide that values by 2 to get the sensor clocks.
### Capture process timings
The next values are in sensor clocks. Multiply by 2 to get Game Boy cycles.
- Reset pulse.
- Configure sensor registers. (11 x 8 CLKs)
- Wait (1 CLK)
- Start pulse (1 CLK)
- Exposure time (exposure_steps x 8 CLKs)
- Wait (2 CLKs)
- Read start
- Read period (N=1 ? 16128 : 16384 CLKs)
- Read end
- Wait (3 CLKs)
- Reset pulse to stop the sensor

88 + 1 + 1 + 2 + 16128 + 3 = 16223

CLKs = 16223 + ( N_bit ? 0 : 256 ) + 8 * exposure

Obviously, that's the previous result divided by 2.
During the read process every pixel is written when it is read from the sensor. If the read process is stopped (by shutting the GB down, for example) the RAM will have the contents of the current picture until the read was stopped, from there it will have the data from the image captured before that one.

The sensor transfers 128×128 pixels, but the upper and lower rows are corrupted. With N=1, the 5 first rows are darker than the rest of the image. The last 6 rows only contain garbage, and the previous row is also darker than the rest of the image.
The Game Boy Camera controller only uses the medium rows of the sensor image. This means that it ignores the first 8 rows and the last 8 rows.
The clock signal during read period must be the same as the one used during the exposure time. If the clock during the read period is too slow the sensor will continue increasing the charge values of each pixel so the image will appear to be taken with a higher exposure time. The brightness doesn't seem to increase always, there seems to be some kind of limit.
# The Game Boy Camera sensor (M64282FP)
The M64282FP does some processing to the captured image. First it performs an edge control, then it does gain control and last it does level control. The resulting analog value is the one that can be read in Vout pin.
## The M64282FP registers
### Register 1

  Symbol Bits Operation
    N 7 Exclusively set vertical edge enhancement mode.
    VH 5,6 Select vertical - horizontal edge operation mode.
    G 0-4 Analog output gain.

Values written at boot: 00, 0A, 20, 24, 28, E4, E8.
When shooting the values change based on how much light there is: 0A, E4, E8.

### Registers 2 and 3
They contain the exposure time (16 bit unsigned value). According to the M64282FP datasheet each step is 16 us. In the GB it needs 16 PHI clocks for every step.
u16 exposure_steps = ([Reg2]<<8) | [Reg3]

Step time = 1 / 1048576 Hz * 16 = 0,954 us * 16 = 15,259 us.

### Registers 4, 5 and 6
They are used by the 1-D processing kernel. They can't be set to any value from the GB Camera cartridge, only to 3 defined sets of values.
[A000]	[4]	[5]	[6]	[4]=P [5]=M [6]=X
1(001)	00h	01h	01h	Negative
3(011)	01h	00h	01h	Positive. This is what the GB Camera ROM uses.
5(101)	01h	02h	01h	Used for edge detection
7(111)	01h	02h	01h	Used for edge detection

The value of X must be fixed to 01h according to the datasheet.

The meaning of this registers is:

### Register 7

    At boot is written (in hex):

        05
        01 02
        03 04 05 06 07
        03 04 05 06 07
        23 24 25 26 27
        23 24 25 26 27
        23 24 25 26 27
        03 04 05 06 07
        05
        08 09 0A 0B 0C 0D 0E 0F
        07 - and stays like that forever (sometimes writes 07 again?)

    This corresponds to this register of M64282FP:

        No. Address 7 6 5 4 3 2 1 0
        7 111 E3 E2 E1 E0 I V2 V1 V0

        Symbol Bit Assignment Operation
        E 4 bits Edge enhancement ratio
        I 1 bit Select inverted/non-inverted output
        V 3 bits Output node bias voltage (Vref)

    At the end:

        E = 0000 - Edge Enhancement Ratio (alpha) = 50% in edge enhancement mode (normal image sensing operation).
        100 % means the same level as the P signal, which is the signal of the central pixel in the
        3x3 processing kernel. Changed during boot for calibrating?
        I = 0 - Normal (non-inverted) output. Changed during boot for calibrating?
        V = 111 - Output node voltage Vref = 3.5 V. Changed during boot for calibrating?

### Register 0

    At boot is written (in hex):

        80
        BF A0 B0 B8 BC BE BF BF
        3F
        BF A0 B0 B8 BC BE BF BF
        BF A0 B0 B8 BC BE BF BF
        BF A0 B0 B8 BC BE BF BF
        BF A0 B0 B8 BC BE BF BF
        BF A0 B0 B8 BC BE BF BF
        80
        BF A0 B0 B8 BC BE BF BF
        3F
        BF -- and stays like that forever (sometimes writes BF again?)

    This corresponds to this register of M64282FP:

        No. Address 7 6 5 4 3 2 1 0
        0 000 Z1 Z0 O5 O4 O3 O2 O1 O0

        Symbol Bit Assignment Operation
        Z 2 bits Zero point calibration ( Set the dark level output signal to Vref )
        O 6 bits Output reference voltage ( In both plus and minus direction )

## M64282FP image processing

Z = '11' is the same as Z = '00'

GAMMA?

Registers 6..35h

        Max Light Min Light
    For example (normal mode, high light): 00112233445566778899AABBCCDDEEFF (input color range 0 - 255)
    - Min. contrast (0): 80 8F D0 -> 00000000000000001122222222233333 (output gb palete 0-3)
    - Med. contrast (7): 89 92 A2 -> 00000000000000000122333333333333
    - Max. contrast (F): 92 92 92 -> 00000000000000000033333333333333
        Black White

    Emulating this would require to emulate the hardware even to know the actual values returned by
    the sensor... Are the input values linear or...?

    Normal mode

    First 3 values of dithering mode, repeated 48/3 = 16 times

    Dithering mode

    High light

Reg 6 7 8 9 A B C D E F 10 11 12 13 14 15 16 17 18 19 1A 1B 1C 1D 1E 1F 20 21 22 23 24 25 26 27 28 29 2A 2B 2C 2D 2E 2F 30 31 32 33 34 35
    Min contrast
    80 8F D0 8B BF E0 82 9B D4 8E CB E4 87 AF DB 83 9F D5 8A BB DF 86 AB D9 81 97 D2 8D C7 E3 80 93 D1 8C C3 E1 89 B7 DD 85 A7 D8 88 B3 DC 84 A3 D6
    82 90 C8 8C BA DC 84 9A CD 8F C4 E1 89 AC D5 85 9E CE 8B B6 DA 88 A8 D3 83 97 CB 8E C1 DF 82 93 C9 8D BD DD 8A B3 D8 87 A5 D2 89 AF D7 86 A1 D0
    84 90 C0 8D B4 D8 86 99 C6 8F BD DE 8A A8 D0 87 9C C8 8C B1 D6 89 A5 CE 85 96 C4 8E BA DC 84 93 C2 8D B7 DA 8B AE D4 88 A2 CC 8A AB D2 87 9F CA
    85 91 B8 8E AE D3 87 98 BE 90 B5 DA 8B A4 CA 88 9A C1 8D AB D1 8A A2 C8 86 95 BC 8F B3 D8 85 93 BA 8E B0 D6 8C A9 CF 89 9F C5 8B A6 CC 88 9D C3
    86 91 B1 8E A9 D0 88 97 B8 90 AF D8 8B A1 C6 88 99 BB 8D A7 CD 8A 9F C3 87 95 B6 8F AD D5 86 93 B3 8E AB D3 8C A5 CB 8A 9D C0 8C A3 C8 89 9B BE
    87 92 AA 8F A4 CC 89 96 B2 91 A8 D5 8C 9E C1 89 98 B5 8E A2 C9 8B 9C BE 88 95 AF 90 A7 D2 87 93 AC 8F A5 CF 8D A1 C6 8B 9B BB 8D 9F C3 8A 99 B8
    88 92 A5 8F A0 C9 89 95 AE 91 A3 D2 8D 9B BD 8A 96 B1 8E 9F C6 8C 9A BA 89 94 AB 90 A2 CF 88 93 A8 90 A1 CC 8E 9D C3 8B 99 B7 8D 9C C0 8B 97 B4
    89 92 A2 8F 9E C6 8A 95 AB 91 A1 CF 8D 9A BA 8B 96 AE 8F 9D C3 8C 99 B7 8A 94 A8 90 A0 CC 89 93 A5 90 9F C9 8E 9C C0 8C 98 B4 8E 9B BD 8B 97 B1
    8A 92 A1 90 9D BE 8B 94 A8 91 A0 C5 8E 99 B4 8C 95 AA 8F 9C BB 8D 98 B2 8B 93 A5 91 9F C3 8A 92 A3 90 9E C0 8F 9B B9 8D 97 AF 8E 9A B6 8C 96 AD
    8B 92 A0 90 9C B6 8C 94 A5 91 9F BC 8E 99 AF 8C 95 A7 8F 9B B4 8E 98 AD 8B 93 A3 91 9E BA 8B 92 A1 90 9D B8 8F 9A B2 8D 97 AB 8E 99 B0 8D 96 A9
    8C 92 9E 90 9B AE 8D 94 A2 91 9D B2 8F 98 A9 8D 95 A3 90 9A AD 8E 97 A7 8C 93 A0 91 9C B1 8C 92 9F 90 9B AF 8F 99 AB 8E 96 A6 8F 98 AA 8D 95 A4
    8D 92 9C 90 99 A8 8D 93 9F 91 9B AB 8F 97 A4 8E 94 A0 90 98 A7 8F 96 A3 8D 93 9E 91 9A AA 8D 92 9D 91 9A A9 90 98 A6 8E 95 A2 8F 97 A5 8E 95 A1
    8E 92 9B 91 98 A2 8E 93 9C 91 9A A4 90 96 A0 8F 94 9D 90 98 A1 8F 95 9F 8E 93 9C 91 99 A3 8E 92 9B 91 99 A3 90 97 A1 8F 95 9E 90 97 A0 8F 94 9E
    8F 92 99 91 97 9E 8F 93 9A 91 98 9F 90 95 9C 8F 93 9A 91 96 9D 90 95 9C 8F 92 99 91 98 9F 8F 92 99 91 97 9E 90 96 9D 90 94 9B 90 95 9C 8F 94 9B
    90 92 97 91 95 99 90 92 97 91 96 99 91 94 98 90 93 97 91 95 99 90 94 98 90 92 97 91 96 99 90 92 97 91 96 99 91 95 98 90 93 98 91 94 98 90 93 97
    92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92 92
    Max contrast

    Low light

Reg 6 7 8 9 A B C D E F 10 11 12 13 14 15 16 17 18 19 1A 1B 1C 1D 1E 1F 20 21 22 23 24 25 26 27 28 29 2A 2B 2C 2D 2E 2F 30 31 32 33 34 35
    Min contrast
    80 94 DC 8F CA F6 83 A1 E2 92 D7 FC 8A B8 ED 85 A6 E4 8D C5 F4 88 B3 EB 82 9D E0 91 D3 FA 81 98 DE 90 CE F8 8C C1 F1 87 AF E9 8B BC EF 86 AA E6
    82 95 D2 90 C2 F3 85 A0 DA 93 CE FC 8B B3 E8 86 A4 DD 8F BE F0 8A AF E5 84 9C D7 92 CA F9 83 98 D4 91 C6 F6 8D BB EE 89 AB E2 8C B7 EB 87 A8 E0
    84 96 CA 91 BD F1 87 9F D3 94 C6 FB 8D B0 E4 88 A3 D7 90 B9 EE 8B AC E1 86 9C D0 93 C3 F8 85 99 CD 92 C0 F5 8F B6 EB 8A A9 DD 8E B3 E7 89 A6 DA
    86 96 C4 92 B8 F0 89 9E CF 95 C1 FB 8E AD E1 8A A1 D2 91 B5 EC 8D AA DD 88 9B CB 94 BE F7 87 98 C7 93 BB F3 90 B2 E8 8C A7 DA 8F AF E5 8B A4 D6
    88 97 BE 93 B4 EE 8A 9E CA 96 BB FA 8F AA DE 8B A0 CE 92 B1 EA 8E A8 DA 89 9B C6 95 B9 F6 88 99 C2 94 B6 F2 91 AF E6 8D A5 D6 90 AC E2 8C A3 D2
    8A 97 B8 93 AF ED 8C 9D C5 96 B5 FA 90 A7 DB 8D 9F C9 92 AD E8 8F A5 D7 8B 9B C0 95 B3 F6 8A 99 BC 94 B1 F1 92 AB E4 8E A3 D2 91 A9 DF 8E A1 CE
    8B 98 B2 94 AB E4 8D 9C BE 97 B0 F0 91 A5 D3 8E 9E C2 93 A9 E0 90 A3 CF 8C 9B BA 96 AE EC 8B 99 B6 95 AD E8 93 A8 DB 8F A1 CB 92 A6 D7 8F A0 C6
    8C 98 AC 95 A7 DB 8E 9B B7 97 AA E7 92 A2 CB 8F 9D BB 94 A5 D7 91 A0 C7 8D 9A B3 96 A9 E3 8C 99 AF 95 A8 DF 93 A4 D3 90 9F C3 92 A3 CF 8F 9E BF
    8D 98 AA 95 A5 D0 8F 9B B3 97 A8 D9 92 A1 C3 8F 9C B6 94 A4 CD 91 9F C0 8E 9A B0 96 A7 D6 8D 99 AD 95 A6 D3 93 A3 C9 91 9E BD 93 A2 C6 90 9D B9
    8E 98 A8 95 A4 C6 8F 9B AF 97 A7 CD 93 A0 BC 90 9C B2 94 A3 C3 92 9F B9 8F 9A AD 96 A6 CB 8E 99 AA 96 A5 C8 94 A2 C1 91 9E B7 93 A1 BE 91 9D B4
    8F 98 A6 95 A2 BC 90 9A AB 97 A5 C2 93 9F B5 91 9B AD 95 A1 BA 92 9E B3 90 99 A9 96 A4 C0 8F 98 A7 96 A3 BE 94 A0 B8 92 9D B1 94 9F B6 91 9C AF
    90 98 A4 96 A1 B4 91 9A A8 97 A3 B8 94 9E AF 92 9B A9 95 A0 B3 93 9D AD 91 99 A6 97 A2 B7 90 98 A5 96 A1 B5 95 9F B1 93 9C AC 94 9E B0 92 9B AA
    92 98 A1 96 9E AD 93 99 A4 97 A0 B0 95 9C A9 93 9A A5 96 9E AC 94 9B A8 92 99 A3 97 9F AF 92 98 A2 96 9F AE 95 9D AB 94 9B A7 95 9D AA 93 9A A6
    94 98 9D 97 9B A5 94 98 9F 97 9C A7 96 9A A2 95 99 9F 96 9B A4 95 9A A1 94 98 9E 97 9C A6 94 98 9D 97 9C A5 96 9B A3 95 99 A1 96 9A A3 95 99 A0
    96 98 99 97 98 9E 96 98 9A 97 98 9F 97 98 9C 96 98 9A 97 98 9D 96 98 9C 96 98 99 97 98 9F 96 98 99 97 98 9E 97 98 9D 96 98 9B 97 98 9C 96 98 9B
    98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98 98
    Max contrast

3x3 programmable 1-D filtering

       +--+
       |MN|
    +--+--+--+
    |MW| P|ME| Out = P + [2P - (MW+ME)] * alpha -> 1D horizontal edge enhancement
    +--+--+--+ Out = P + [4P - (MN+MS+ ME+ MW)] * alpha -> 2D edge enhancement
       |MS|
       +--+ alpha = 0.5 (?)

    Not really sure of which is used but, by looking at the result in the GB Camera game and some tests
    done in the emulator by changing the filters, it seems that the 2D edge enhancement is the one used.

    With this configuration: Out = 2P - [ (MW+ME) / 2 ]
        Out = 3P - [ (MN+MS+ME+MW) / 2 ]